Long runs protocol

- Molecular dynamics software – LAMMPS
- Force fields:
  - Cu
    - Lennard-Jones (LJ), using parameters from “The molecular dynamic simulation on impact and friction characters of nanofluids with many nanoparticles system”, https://www.researchgate.net/figure/LJ-potential-parameters-for-simulation_tbl1_51450660
  - Octadecene
    - United atom model using LJ, parameters calculated using the TraPPE model, “Transferable Potentials for Phase Equilibria. 4. United-Atom Description of Linear and Branched Alkenes and Alkylbenzenes”,
      https://pubs.acs.org/doi/10.1021/jp001044x
    - Coarse grained using LJ, parameters from “Supra-Atomic Coarse-Grained GROMOS Force Field for Aliphatic Hydrocarbons in the Liquid Phase”,
      https://pubs.acs.org/doi/10.1021/acs.jctc.5b00295
  - Hexadecane
    - Coarse grained using LJ, parameters from “Supra-Atomic Coarse-Grained GROMOS Force Field for Aliphatic Hydrocarbons in the Liquid Phase”,
      https://pubs.acs.org/doi/10.1021/acs.jctc.5b00295
- Structure desing:
  - xyz files for Cu and united atom octadecene created using Avogadro, pdb files created using OpenBabel at:
    http://www.cheminfo.org/Chemistry/Cheminformatics/FormatConverter/index.html,
- Runs details:
  - noAdditive5000
    - Initial locations generated using Packmol
    - Started with npt with T=520, Tdamp=100, P=1, Pdamp=1000, timestep=1, duration 2ns, Cu:solvent=1:50, replicate = 17^3
    - Checked energy convergence with nve, 100,000 steps.
  - Coarse-grained hexadecane
    - Mixing: 60 molecules of hexadecane using replicate, 1 atom of copper put randomly. Mixing runs were done in npt in atmospheric pressure. Ran 0.5 ns in 300K, heated to 520 K in 1.5 ns, ran 0.5 ns in 520K.
    - Start: replicate 16^3 the mixed solution in 520 K, ran for 1 ns in npt with T=520, Tdamp=100, P=1, Pdamp=1000 timestep = 0.25fs.
    - Failed to converge energy with longer timestep; rate of ~3.5 ns/day.
  - Coarse-grained octadecene
    - Mixing: 60 molecules of octadecene using replicate, 1 atom of copper put randomly. Mixing runs were done in npt in atmospheric pressure. Ran 0.5 ns in 300K, heated to 520 K in 1.5 ns, ran 0.5 ns in 520K.
    - Start: replicate 16^3 the mixed solution in 520 K, ran for 1 ns in npt with T=520, Tdamp=100, P=1, Pdamp=1000 timestep = 0.25fs.
    - Failed to converge energy