- Molecular dynamics software – LAMMPS
- Force fields:
  - Cu
    - Lennard-Jones (LJ), using parameters from “The molecular dynamic simulation on impact and friction characters of nanofluids with many nanoparticles system”, https://www.researchgate.net/figure/LJ-potential-parameters-for-simulation_tbl1_51450660
  - Octadecene
    - United atom model using LJ, parameters calculated using the TraPPE model, “Transferable Potentials for Phase Equilibria. 4. United-Atom Description of Linear and Branched Alkenes and Alkylbenzenes”,
      https://pubs.acs.org/doi/10.1021/jp001044x
    - Coarse grained using LJ, parameters from “Supra-Atomic Coarse-Grained GROMOS Force Field for Aliphatic Hydrocarbons in the Liquid Phase”,
      https://pubs.acs.org/doi/10.1021/acs.jctc.5b00295
  - Triphenylphosphite
    - Full description using LJ, GAFF2 force field calculated using pysimm package
    - United atom model for the phenyl’s CH sites using LJ. LJ coefficients for CH sites and bond/angle coefficients were taken from the TraPPE model for this kind of aromatic CH sites. Other LJ coefficients are the same as in the full atom description
- Structure desing:
  - Full description using Avogadro
  - United atom using TraPPE model’s tool in http://trappe.oit.umn.edu/#UA
- Runs:
  - smallBias – 216 atoms of copper, SIGMA=0.0002 PACE=100 HEIGHT=2.2, timestep 1fs, lost atoms after 1 ns.
  - SmallBiasWithAdditive - 216 atoms of copper, timestep 0.25fs, lost atoms in the mixing stage at 520K.
  - RtsmallBias – mix 1 atom of copper in 60 molecules of octadecene for 1 ns in 300K, replicate 216 times the basic cell and run for another 2 ns.
  - RtsmallHexane – mix 1 atom of copper in 60 molecules of hexane for 1 ns in 200K heat to 270K for 2 ns, mix for another 1 ns. Replicate 216 times the basic cell and run for another 2 ns.